## Slide 1: Analog Communication
UNIT – III
Made by: Hridesh Vishwdewa
Tweneboah-Koduah Samuel

## Slide 2: AC4D
Modulation Fundamentals

## Slide 3
Power Spectra Density (PSD)
Energy Spectra Density (ESD)
Noise Equivalent Bandwidth
Ergodic Process
Frequency Response of LTI systems
Sampling Theorem
Fourier Series and Transform
Note: The following topics are left for later consideration or treatment.
However, students are encouraged to read about them.

## Slide 4: Modulation Techniques

## Slide 5: Frequency translation
Suppose that a signal is bandlimited to the frequency range extending from a frequency f1 to f2.
Frequency translation is used to replace the signal with a new signal whose spectral range extends from f1’ to f2’ and has a recoverable form the same info as was within the original

## Slide 6: Method of frequency translation
A signal may be translated to a new spectral range by multiplying the signal with an auxiliary sinusoidal signal.
Let’s take a signal
The two sided spectral amplitude pattern is as shown below (a)
Euler’s theorem
Notes: Where Am is the constant amplitude

## Slide 7: Method of frequency translation
Let’s multiply vm(t) with an auxiliary signal vc(t)
The new spectral amplitude pattern is shown in (b).
Observe that the two original spectral lines have been translated, both in the positive-frequency direction by amount fc and also in the negative-frequency direction by the same amount.
There are now four spectral components resulting in two sinusoidal waveforms, one of frequency fc + fm and the other of frequency fc - fm with amplitude each
Notes: Fourier transform can be used to achieve the same results

## Slide 8: Recovery of the baseband signal
Recovery original signal m(t) from a translated version
The recovery may be done by reverse translation, which is accomplished by simply multiplying the translated signal with
The baseband signal m(t) reappears. The higher order frequency (double-freq. signal) which has fc >> fm is easily removed by a LPF
Notes: ■8([𝑚(𝑡)cos𝜔_𝑐 𝑡]cos𝜔_𝑐 𝑡=𝑚(𝑡)cos^2 𝜔_𝑐 𝑡=𝑚(𝑡)(1/2+1/2 cos2𝜔_𝑐 𝑡)@=├ 𝑚(𝑡)/2+├ 𝑚(𝑡)/2 cos2𝜔_𝑐 𝑡)

## Slide 9: Modulation Fundamentals

## Slide 10: Modulation fundamental
Before an information-bearing signal is transmitted through a communication channel, some type of modulation process is typically utilized to produce a signal that can easily be accommodated by the channel.
The modulation process commonly translates an information-bearing signal, usually referred to as the message signal, to a new spectral location depending upon the intended frequency for transmission.
Multiplexing allows two or more message signals to be transmitted by a single transmitter and received by a single receiver simultaneously.
The two basic types of analog modulation are continuous-wave modulation and pulse modulation. In continuous-wave modulation, a parameter of a high-frequency carrier is varied proportionally to the message signal such that a one-to-one correspondence exists between the parameter and the message signal.

## Slide 11: Modulation fundamental
The message signal is called a modulating signal. Modulation converts the message signal m(t) from lowpass to bandpass, in the neighborhood of the carrier (centre) frequency fc
For a sinusoidal carrier, a general modulated carrier can be represented as
where is the carrier frequency
The component of the carrier signal that can be varied in the modulation process is
  The instantaneous amplitude A(t) and
  Phase deviation .
When the amplitude A(t) is linearly related to the modulating signal, the result is linear modulation. E.g. AM
Letting f(t) or the time derivative of f(t) be linearly related to the modulating signal yields phase or frequency modulation, respectively.
Collectively, phase and frequency modulation are referred to as angle modulation, since the instantaneous phase angle of the modulated carrier conveys the information.

## Slide 12: Modulation fundamental
Modulation is the process of changing some characteristics (amplitude, frequency and phase) of carrier wave in accordance with the instantaneous value of the modulating signal m(t)
Types of modulation
  Amplitude modulation
  Frequency modulation
  Phase modulation

## Slide 13: Modulation fundamental
Why modulation necessary?
  Signals that occupy the same range of frequency can be separated
  Modulation helps in noise immunity, attenuation – depends on the physical medium
Advantages of modulation
  Reduces antenna height
  Height of antenna is a fraction of wavelength. The minimum height of antenna is given by
  Avoid mixing of signals
  Increase range of communication
    Modulation increases the frequency of the signal allowing it to be transmitted over long distance
  Allow multiplexing of signals
    multiplexing (sometimes contracted to mixing) is a method by which multiple analog message signals or digital data streams are combined into one signal over a shared medium.
  Allows adjustments in the bandwidth
    Bandwidth of a modulated signal may be made smaller or larger
  Improve the quality of reception
    Modulation reduces the effect of noise to improve quality of reception
Notes: 𝜆∕4

## Slide 14: Assignment
The capacity in bits per second of an addictive white Gaussian noise (AWGN) channel is
where P is the received signal power, B is the signal bandwidth, and No/2 is the noise power spectral density. The total noise is given by . Consider a wireless channel where received power falls off with distance d according to the .
Given do = 10 m, transmitter power Pt = 1W, noise PSD No = 10-9 W/Hz and channel bandwidth of B = 30 kHz, find the capacity of the channel for transmitter-receiver distance of 100m and 1 km.
Find the average power of the signal shown below

## Slide 15: Amplitude modulation (AM)
The analogue signal to be transmitted is denoted by m(t), which is assumed to be a lowpass signal of bandwidth W, i.e., M(f) ≡ 0, for |f| > W. Let’s assume that the signal is a power-type signal whose power denoted by Pm, is
Or
Finite periodic signal

## Slide 16: Amplitude modulation (AM)
The message m(t) is transmitted through the communication channel by impressing it on a carrier or bandpass signal of the form
Let for AM
Depending on the relationship between m(t) and Ac(t), we have various types of AM schemes
  Double-sideband (DSB) modulation
  Single-Sideband (SSB)
  Vestigial-Sideband (VSB) modulation
  Convention or Ordinary AM
Notes: 𝑔(𝑡)=𝐴_𝑐 [├ 1+𝑚(𝑡)]

## Slide 17: Amplitude modulation (AM)
The message m(t) is transmitted through the communication channel by impressing it on a carrier or bandpass signal of the form
Let for AM
The conventional AM modulated signal is
The AM modulated signal is normally written as
where is called complex envelop of AM signal
is the amplitude sensitivity of the modulator measured in per volts
Notes: 𝑔(𝑡)=𝐴_𝑐 [├ 1+𝑚(𝑡)]

## Slide 18: Amplitude modulation (AM)
Effects of ka – the modulation sensitivity
for all t
for all t
For all t, we overmodulation
Carrier phase reverse whenever the factor crosses the time axis or zero
Notes: for all t, the carrier becomes over modulated resulting in carrier phase reversal whenever the factor crosses the time axis or zero
|├ 𝑘_𝑎 𝑚(𝑡)|>1 for all t, the carrier becomes over modulated resulting in carrier phase reversal whenever the factor ├ 1+𝑘_𝑎 𝑚(𝑡) crosses the time axis or zero

## Slide 19: Amplitude modulation (AM)
Effect of carrier frequency
The detection and visualization of the envelop demands
where W is the message bandwidth
Taking FT of the AM wave s(t), we get

## Slide 20: Amplitude modulation (AM)
Suppose the baseband signal m(t) is bandlimited to the interval (Fig a).
Fig b for  This spectrum consist of two delta functions weighted by and occurring at , scaled in amplitude by by
Notes: ±𝑓_𝑐

## Slide 21: Example
A 1.4-MHz carrier is modulated by a music signal that has frequency components from 20 Hz to 15 kHz. Determine the range of frequencies generated for the upper and lower sidebands.
Solution
The upper side band is equal to the sum of carrier and intelligence frequencies. Therefore, the upper side band (usb) will include the frequencies from

## Slide 22: Example
A 1.4-MHz carrier is modulated by a music signal that has frequency components from 20 Hz to 15 kHz. Determine the range of frequencies generated for the upper and lower sidebands.
Solution
The upper side band is equal to the sum of carrier and intelligence frequencies. Therefore, the upper side band (usb) will include the frequencies from

## Slide 23: AM modulation index
For undistorted AM to occur, the modulating signal voltage must be less than the carrier voltage
Therefore the relationship between the amplitude of the modulating signal and the amplitude of the carrier signal is important.
This relationship, known as the modulation index m (also called the modulating factor or coefficient, or the degree of modulation)
The modulation index is given by
Notes: The ratio of change in amplitude of modulating signal to the amplitude of carrier wave is know as modulation index or factor

## Slide 24: AM modulation index
Modulation index in terms of amplitude sensitivity using time domain description
Let be the message signal
Carrier signal is
The standard AM wave is given as before
Putting m(t) in s(t) yields
is called modulation index
Eqn1
Notes: Expanding eqn-1
and using trig identities 
The results consist of three frequency components
Expanding eqn-1
├ 𝑠(𝑡)=𝐴_𝑐 cos(2𝜋𝑓_𝑐 𝑡)+𝜇𝐴_𝑐 cos(2𝜋𝑓_𝑐 𝑡)·cos(2𝜋𝑓_𝑚 𝑡)
and using trig identities 
cos𝐴cos𝐵=1/2 [├ cos(𝐴−𝐵)+cos(𝐴+𝐵)]
The results consist of three frequency components

## Slide 25: AM modulation index
Let Ei = Em, B = Emax, A = Emin
Emax is the maximum voltage peak-to-peak AM signal
Emin is the minimum voltage peak-to-peak AM signal
m is the modulation index

## Slide 26: AM modulation index
Percentage modulation
Over-modulation
If the AM waveform’s minimum value Emin falls to 0 then
 Em is greater than Ec
Over-modulation generate a “gap” in the modulated signal, which produces distortion called side-band splatter which results in the transmission of frequencies outside of a station's normal allocated range.

## Slide 27: AM power and efficiency
Given that the total normalize power of a bandpass signal as , where g(t) is the envelop of AM wave
The normalized average power of AM signal is
For no DC level, the power is
Carrier power, Pc
Sideband power, Ps

## Slide 28: AM power and efficiency
Modulation efficiency or power efficiency is the percentage of the total power of the modulated signal that conveys information.
In AM signaling, only the sideband components convey information, so the modulation efficiency is

## Slide 29: Example
A carrier wave of frequency 15 MHz and peak value 15 V is amplitude by a 5 KHz sine wave of amplitude 8 V. Find the modulation index and draw the corresponding spectrum
Notes: Continue from handout page 50

## Slide 30: Bandpass transmission system
Bandpass signal xbp(t) applied to a bandpass system with transfer function Hbp( f ) produces the bandpass output ybp(t)
The simplest bandpass system is the parallel resonant or tuned circuit represented

## Slide 31: Bandpass transmission system
The simplest bandpass system is the parallel resonant or tuned circuit represented
Where fo is the resonant freq. and Q is the quality factor. These are related by
The 3 dB bandwidth between the lower and upper cutoff frequencies
Notes: Transfer function
The fractional bandwidth should be kept within the range of
Otherwise the serious signal distortion can occur
Transfer function 𝐻(𝑓)=1/(1+𝑗𝑄(𝑓/𝑓_𝑜 −𝑓_𝑜/𝑓) )
The fractional bandwidth should be kept within the range of
0.01<𝐵/𝑓_𝑐 <0.1
Otherwise the serious signal distortion can occur

## Slide 32: AM Detailed power calculation
Expanding
Carrier power

## Slide 33: Virtues and limitation of Conventional AM
Generation and detection is very easy
It is very cheap to build.
AM is wasteful of power
  Due to transmission of carrier wave which is independent of intelligent signal
AM is wasteful of bandwidth
  The transmission of both upper and lower sideband which are uniquely related by virtue of their symmetry about the fc, one can be determined from the other.

## Slide 34: Generation of AM waves
AM wave generation requires two basic methods
  Square-Law modulator
  Switching modulator
Others
  Balanced modulator (Square Law variant)
  Ring Modulator (Switching variant)
  etc

## Slide 35: Square-law modulator
Notes: What’s a nonlinear device?

## Slide 36: Square-law modulator
Square-law modulator consist of
  Summer: It adds the carrier and the modulating signal
  Non-linear device: a device with non-linear i/p –o/p relation
  Band-pass filter (BPF): This extract the deserved signal from the modulator product
The total i/p signal is
Notes: 𝑉_𝑜=𝑎_𝑜+𝑎_1 𝑉_𝑖𝑛+𝑎_2 𝑉_𝑖𝑛^2+𝑎_3 𝑉_𝑖𝑛^3+...

## Slide 37: Square-law modulator
Nonlinear device:- When the output of a device is not directly proportional to input throughout the operation, the device is said to be non-linear.
The Input-Output relation of a non-linear device can be expressed as
When the input is very small, the higher power terms can be neglected, hence
When the output is considered up to square of the input, the device is called a square law device.
Notes: The a’s are constant

## Slide 38: Square-law modulator
Consider a nonlinear device to which a carrier and info signal m(t) fed simultaneously into the square law modulator.
The total i/p signal is
Notes: 𝑉_𝑜=𝑎_𝑜+𝑎_1 𝑉_𝑖𝑛+𝑎_2 𝑉_𝑖𝑛^2+𝑎_3 𝑉_𝑖𝑛^3+...

## Slide 39: Square-law modulator
The required AM signal with a carrier freq. fc can be separated using a bandpass filter at the o/p of square law device.
The filter o/p is
If , we get
Comparing this with the standard representation of AM signal
Therefore modulation index of the output signal is given by
Notes: 𝑉_𝑜=𝑎_𝑜+𝑎_1 𝑉_𝑖𝑛+𝑎_2 𝑉_𝑖𝑛^2+𝑎_3 𝑉_𝑖𝑛^3+...

## Slide 40: Switching modulator
Consider a semiconductor diode used as an ideal switch to which a carrier wave c(t) and message signal m(t) are simultaneously applied.
The total input signal at the diode terminal at any instant is

## Slide 41: Switching modulator
When the peak amplitude of c(t) is maintained more than that of information signal, the operation is assumed to be dependent on only c(t) irrespective of m(t).
When c(t) is positive, v2 = v1 since the diode is forward biased.
Similarly, when c(t) is negative, v2 = 0 since diode is reverse biased.
Based upon the above operation, switching response of the diode is periodic rectangular wave with an amplitude of unity.
The o/p of the diode is

## Slide 42: Switching modulator
The required AM signal centered at fc can be separated using band pass filter.
.
The filter output is given by the ff equation
The diode response Vo, is a product of switching response p(t) and input v1

Thus,
Notes: 𝑣_2=[├ 𝐴_𝑐 cos2𝜋𝑓_𝑐 𝑡+𝑚(𝑡)][1/2+2/𝜋 cos2𝜋𝑓_𝑐 𝑡−2/3𝜋 cos6𝜋𝑓_𝑐 𝑡+−+−]

## Slide 43: Switching modulator
The required AM signal centered at fc can be separated using band pass filter.
The filter output is given by
Notes: The lower cutoff-frequency for the band pass filter should be between w and fc – w and the upper cut-off frequency between fc + w and 2fc.
The lower cutoff-frequency for the band pass filter should be between w and fc – w and the upper cut-off frequency between fc + w and 2fc.
𝑣_2=[├ 𝐴_𝑐 cos2𝜋𝑓_𝑐 𝑡+𝑚(𝑡)][1/2+2/𝜋 cos2𝜋𝑓_𝑐 𝑡−2/3𝜋 cos6𝜋𝑓_𝑐 𝑡+−+−]

## Slide 44: AM Demodulation – Envelop detector
Demodulation is the process of recovering the information signal (baseband) from the incoming modulated signal at the receiver.
There are two methods:
Square law demodulator and
Envelop detector

## Slide 45: AM Demodulation – Envelop detector
Envelope detector is a simple and highly effective device use to demodulate AM wave.
It consist of diode and a resistor capacitor (RC) filter

## Slide 46: AM Demodulation – Envelop detector
During the positive half cycles of the input signals, the diode D is forward biased and the capacitor C charges up quickly to the peak of the input signal.
When the input signal falls below this value, the diode becomes reverse biased and the capacitor C discharges through the load resistor RL.
The discharge process continues until the next positive half cycle.
When the input signal becomes greater than the voltage across the capacitor, the diode conducts again and the process is repeated.

## Slide 47: AM Demodulation – Envelop detector
Selection of RC time constant:
  The capacitor charges through Rs when the diode is on, and discharges through RL when the diode is off.
  The charging time constant should be short or small as compared to the carrier period . i.e. . So that the capacitor charges quickly.
  The discharging time constant should be large to ensure that the capacitor discharges slowly through the load resistor RL between positive peak of the carrier wave. i.e. , where W is max modulating freq.
The result is that the capacitor voltage or detector output is nearly the same as the envelope of AM wave
Notes: 1/𝑓_𝑐 ≪𝑅_𝐿 𝐶≪1/𝑊

## Slide 48: DSB-SC Modulation
DSB-SC is obtained by product modulator that simply multiples the message signal m(t) by the carrier wave

## Slide 49: DSB-SC Modulation
The modulated signal s(t) undergoes phase reversal whenever the message signal m(t) crosses zero

## Slide 50: Example
Suppose that the modulating signal m(t) is a sinusoid of the form
Determine the DSB-SC AM signal and its upper and lower sidebands.
Take
Notes: Handout page 44
├ 𝑐(𝑡)=𝐴_𝑐 cos(2𝜋𝑓_𝑐 𝑡+𝜙_𝑐 )

## Slide 51: Self-check
A signal m(t) bandlimited to 5 kHz is DSB modulated by to yield s(t). For what value of carrier frequency fc, will the bandwidth of s(t) be 2% of fc

## Slide 52: Power content of DSB-SC signal
Taking the DSB signal, the power content can be calculated by taking time-average autocorrelation function as
FT of gives
The power-spectral density of the DSB-SC signal is the power- spectral density of the message shifted upward and downward by fc and scaled by
Notes: Next Total power of DSB

## Slide 53: Power content of DSB-SC signal
The total power of DSB signal can be found by setting in the autocorrelation function or
The power can be determined by integrating over all frequency components.
Using for gives
Where is the power of the message signal

## Slide 54: Self-check
Determine the power-spectral density of the modulated signal, the power in the modulated signal, and the power in each of the sidebands. Given the modulated signal as
Notes: ├ 𝑠(𝑡)=𝐴_𝑐 𝐴_𝑚 cos(𝜔_𝑚 𝑡)cos(𝜔_𝑐 𝑡+𝜙_𝑐 )

## Slide 55: Demodulation of DSB-SC
In the absence of noise and ideal channel, the received signal is equal to the modulated signal
Demodulation is done by multiplying r(t) by a sinusoid
Pass the resulting signal through ideal LPF with bandwidth W
Notes: ■8(@├ ┤) )

## Slide 56: Demodulation of DSB-SC
The LPF rejects higher freqs.
Hence, the o/p is
How do we recover the intelligent signal from this received signal with phase difference or the factor ?
We require phase-coherent or synchronous demodulator to recover message signal m(t) from the received signal. 
This is done by adding a carrier component called “pilot tone” to the transmitted signal in a phase-locked technique
Another way is to use phase-locked loop at the receiver end

## Slide 57: Demodulation of DSB-SC
Coherent detector
The message signal m(t) can be uniquely recovered from a DSBSC wave s(t) by first multiplying s(t) with a locally generated sinusoidal wave and then low pass filtering the product as shown.
It is assumed that the local oscillator signal is exactly coherent or synchronized, in both frequency and phase, with the carrier wave c(t) used in the product modulator to generate s(t).
This method of demodulation is known as coherent detection or synchronous detection.

## Slide 58: Demodulation of DSB-SC

## Slide 59: Demodulation of DSB-SC
From the spectrum, it is clear that the unwanted component (first term in the expression) can be removed by the low-pass filter, provided that the cut-off frequency of the filter is greater than W but less than 2fc-W.
The filter output is given by

## Slide 60: Demodulation of DSB-SC
Costas receiver or Costas loop
Costas receiver is a synchronous receiver system, suitable for demodulating DSBSC waves. It consists of two coherent detectors supplied with the same input signal but with individual local oscillator signals that in phase quadrature w.r.t. to each other as indicated in the image above
Notes: Costas receiver is a synchronous receiver system, suitable for demodulating DSBSC waves. It consists of two coherent detectors supplied with the same input signal but with individual local oscillator signals that in phase quadrature w.r.t. to each other as indicated in the image above

## Slide 61: DSB-SC
Advantages
Low Power consumption or power saying.
The modulation system is simple.
Efficiency is more than AM
Carrier wave is suppressed
Linear modulation type is required
It can be used for point to point communication
Disadvantages
Design o f receiver is complex
Bandwidth required is same as that o f AM
Application
Analogue TV systems to transmit color information

## Slide 62: Single side-band suppressed carrier modulation (SSB-SC)
Standard AM and DSB-SC require transmission bandwidth equal to twice the message bandwidth.
In both cases, the spectrum contains two side bands of width W Hz, each.
However, the upper and lower sides are uniquely related to each other by the virtue of their symmetry about the carrier frequency.
That is, given the amplitude and phase spectra of either side band, the other can be uniquely determined.
No information is lost when only one side band is transmitted, and both the carrier and the other side band are suppressed at the transmitter.
This kind of modulation is called SSB-SC

## Slide 63: Single side-band suppressed carrier modulation (SSB-SC)
The selection of the sideband is done by using Hilbert transform filter

## Slide 64: Assignment
Consider a message signal V and a carrier signal V
  Find the resulting AM wave for 75% modulation
  Sketch the spectrum of this AM wave
  Find the power developed across a load of 150 Ω
Notes: ├ 𝑐(𝑡)=50cos(100𝜋𝑡)

## Slide 65: Assignment
An AM signal has the form u(t) = [20 + 2cos3000πt + 10cos6000πt]cos2πfct, where fc = 105Hz.
Sketch the spectrum of u(t)?
Determine the power in each of the frequency components?
Determine the modulation index?
Determine the power in the sidebands, the total power, and the ratio of the sidebands power to the total power?
Notes: ├ 𝑐(𝑡)=50cos(100𝜋𝑡)

## Slide 66: Angle Modulation FM & PM

## Slide 67: Angle modulation
Angle modulation is a method of analog modulation in which either the phase or frequency of the carrier wave is varied according to the message signal.
In this method of modulation the amplitude of the carrier wave is maintained constant.
Let denote the angle of modulated signal sinusoidal carrier, assumed to be a function of the message signal.
In general, angle modulated signal is of the form
Notes: 𝑠(𝑡)=𝐴_𝑐 cos[├ 𝜃_𝑖 (𝑡)]

## Slide 68: Angle modulation
Where Ac is the amplitude of the carrier wave and
is the angle of the modulated carrier and also the function of the message signal.
The instantaneous frequency of the angle modulated signal, s(t) is given by
Notes: 𝑓_𝑖 (𝑡)=1/2𝜋 ├ 𝑑𝜃_𝑖 (𝑡)/𝑑𝑡

## Slide 69: Angle modulation
Since s(t) is a bandpass signal, it can be represented as
The instantaneous frequency of the angle modulated signal, s(t) is given by
If m(t) is the message signal, then in a PM system we have
and in FM, we have
Where kp and kf are phase and freq, deviation constant
Notes: is the phase of the signal
𝜙(𝑡) is the phase of the signal

## Slide 70: Angle modulation
Comparison of PM and FM modulators
We can then write this from the above analysis
There are two commonly used methods of angle modulation: 1. Frequency Modulation, and 2. Phase Modulation.
Notes: is the phase of the signal
𝜙(𝑡) is the phase of the signal

## Slide 71: Example – Deriving PM & FM waves
A message signal is given by is used to either freq. modulate or phase modulate a carrier . Find the modulated signal in each case
Solution. Using
Solution continues on the board
Notes: 𝑐(𝑡)=𝐴_𝑐 cos(2𝜋𝑓_𝑐 𝑡

## Slide 72: Frequency modulation
Taking the general FM wave
And the angle of modulated carrier is

Depending on the value of mod. index , we get two cases of FM
  Narrowband FM  << compared to one radian (ie << 1) or << 1
  Wideband FM  >> compared to one radian (ie >> 1) or >> 1
Notes: 𝑠(𝑡)=𝐴_𝑐 cos[├ 2𝜋𝑓_𝑐 𝑡+𝛽sin(2𝜋𝑓_𝑚 𝑡)]

## Slide 73: Narrowband FM
Taking the general FM wave
  If m(t) and kf are such that for all t, << 1, then we can expand and simplifying s(t) to a simple approximation as
This is an approximate form of a narrowband FM wave produce by a sinusoidal modulating signal,
Notes: ├ 𝑠(𝑡)=𝐴_𝑐 cos2𝜋𝑓_𝑐 𝑡−𝛽𝐴_𝑐 sin(2𝜋𝑓_𝑐 𝑡)sin(2𝜋𝑓_𝑚 𝑡)

## Slide 74: Narrowband FM
Using trig. identities, s(t) is
The above equation represents the NB-FM signal.
This representation is similar to an AM signal, except that the lower side frequency has negative sign.
Notes: 𝑠(𝑡)=𝐴_𝑐 cos2𝜋𝑓_𝑐 𝑡+(𝛽𝐴_𝑐)/2 [cos(2𝜋(𝑓_𝑐+𝑓_𝑚)𝑡)−cos(2𝜋(𝑓_𝑐−𝑓_𝑚)𝑡)]

## Slide 75: Narrowband FM
The magnitude spectrum of NB-FM signal is as shown below,  this is similar to AM signal spectrum.
The bandwidth of the NB-FM signal is 2fm, which is same as AM signal
Notes: 𝑠(𝑡)=𝐴_𝑐 cos2𝜋𝑓_𝑐 𝑡+(𝛽𝐴_𝑐)/2 [cos(2𝜋(𝑓_𝑐+𝑓_𝑚)𝑡)−cos(2𝜋(𝑓_𝑐−𝑓_𝑚)𝑡)]

## Slide 76: We skip Wideband FM

## Slide 77: Bessel function
The plot below is for different n and
The equation for the complex envelop of FM (esp. WB-FM) is
Taking the real value of s(t), we get
The angle-modulated signal contains all frequencies of the for
This means the actual bandwidth of the s(t) is infinite.
However, the amplitude for sinusoidal components with for large n is small so effective bandwidth is define for s(t)
Note:
Notes: 𝑛=0,±1,±2,...

## Slide 78: Bessel function
The plot below is for different n and

## Slide 79: Bessel function
The plot below is for different n and
Table of Bessel functions
Notes: 𝑠 ̃(𝑡)=𝐴_𝑐 ∑129_(𝑛=−∞)^∞▒├ 𝐽_𝑛 (𝛽)exp(𝑗2𝜋𝑛𝑓_𝑚 𝑡)

## Slide 80: Power content of FM
The power content of FM carrier signal is given by
The power content of modulated carrier or FM wave is
Notes: For small value of B (beta) the function goes to 1

## Slide 81: Example
Let the carrier be given by c(t) = 10cos(2πfct) and let the message signal be cos(20πt)
Further assume that the message is used to frequency modulate the carrier with kf = 50.
Find the expression for the modulated signal and determine how many harmonics should be selected to contain 99% of the modulated signal power.
Solution on the board

## Slide 82: Transmission bandwidth of FM
For FM signal generated by a single tone modulating signal of freq. fm, we can define approximate rule for the transmission bandwidth using Carson’s rule 
If the message signal is given by
Notes: In theory, an FM signal contains an infinite number of side frequencies so that the bandwidth required to transmit such a signal is similarly infinite in extent. In practice, however, we find that the FM signal is effectively limited to a finite number of significant side frequencies compatible with a specified amount of distortion. We may therefore specify an effective bandwidth required for the transmission of an FM signal.

## Slide 83: Example
Estimate BFM for the modulating signal m(t) in the figure below for and modulating freq. (W) of 15 kHz
Notes: 𝑘_𝑓=2𝜋×〖10〗^5

## Slide 84: Self-check
Repeat the problem of the example on the previous slide if the amplitude of m(t) is doubled [ie. if m(t) is multiplied by 2]
Notes: 𝑘_𝑓=2𝜋×〖10〗^5

## Slide 85: Self-check
An angle-modulated signal with carrier frequency is described by the equation
Find the power of the modulated signal
Find frequency deviation
Find the deviation ratio
Find the phase deviation
Estimate the bandwidth of
Note: The bandwidth is 1000 Hz, the highest freq. in m(t)
Find the instantaneous freq. first
By differentiation 
Find max carrier deviation  get freq. deviation
 We need
 Carson’s formula
Notes: Pulse to explain
Note: The bandwidth is 1000 Hz, the highest freq. in m(t)
The two sinusoidal you get after derivative could add up at some point in time  we take their amplitude and add
The sum of the amplitudes of the sinusoid gives the phase deviation

## Slide 86: Example
Find the bandwidth of a single tone modulated FM signal described by
Solution
Notes: 𝑠(𝑡)=10cos[├ 2𝜋〖10〗^8 𝑡+6sin(2𝜋〖10〗^3 𝑡)]

## Slide 87: Angle modulators
One method for generating an FM signal directly is to design an oscillator whose frequency changes with the input voltage.
When the input voltage is zero, the oscillator generates a sinusoid with frequency fc, and when the input voltage changes, this frequency changes accordingly.
There are two approaches to designing such an oscillator, usually called a VCO or voltage-controlled oscillator. One approach is to use a varactor diode and reactance tube.
Others include indirect method which makes used of NB-FM signal

## Slide 88: FM Generation cont’d
Voltage-Controlled Oscillator

## Slide 89: Varactor diode VCO
A varactor diode is a capacitor whose capacitance changes with the applied voltage
If this capacitor is used in the tuned circuit of the oscillator and the message signal is applied to it, the frequency of the tuned circuit, and the oscillator, will change in accordance with the message signal
Simplified
Notes: What is varactor diode?

## Slide 90: Varactor diode VCO
Let set the inductor value to Lo the capacitance of the varactor diode as
Now, when m(t) = 0, the freq. of the tuned circuit is
In general for nonzero m(t)
Notes: What is varactor diode?
What is varactor diode?
𝑓_𝑐=1/(2𝜋√(𝐿_𝑜 𝐶_𝑜 ))

## Slide 91: Indirect Armstrong transmitter

## Slide 92: Application of FM
Some of the applications of the FM modulation are listed below:
  FM Radio,(88 -108 MHz band, 75 kHz)
  TV sound broadcast, 25 kHz,
  Two-way mobile radio, 5 kHz / 2.5 kHz.

## Slide 93
Carrier
Intelligent signal
FM wave
PM wave

## Slide 94: Advantages and disadvantages of FM over AM
Advantages of FM over AM are:
  Less radiated power.
  Low distortion due to improved signal to noise ratio (about 25dB) w.r.t. to man made interference.
  Smaller geographical interference between neighboring stations.
  Well defined service areas for given transmitter power.
Disadvantages of FM:
  Much more Bandwidth (as much as 20 times as much).
  More complicated receiver and transmitter.

## Slide 95: Comparison of FM and AM
FM | AM
The modulation index can have value either less than one or more than one. | The value of modulation index is always between zero and one.
Since in FM, amplitude of the earner is constant, the transmitted power is constant, independent of the modulation index. | Transmitted power is dependent upon modulation index
The modulation index determines the number of significant pairs of sidebands in an FM signal. | In an AM signal, only two sidebands are produced, for any value of modulation index.
The amplitudes of the carrier and side bands vary with the modulation index and can be calculated with Bessel functions. | The amplitudes of the sidebands is dependent on the modulation index, and is always less than the amplitude of carrier.
The carrier or sideband amplitudes are zero at some modulation indices. | The sideband amplitude is never zero for any value of modulation index greater than zero.
The bandwidth of an FM signal is proportional to the modulation index. | The bandwidth of an AM signal is twice the highest modulating frequency.
For FM, the % of modulation is the ratio of the actual frequency deviation and the maximum.om permissible frequency deviation multiplied by 100. | For AM, % modulation is the ratio of amplitude of modulating voltage to the amplitude of the carrier multiplied by 100.
FM | AM
The modulation index can have value either less than one or more than one. | The value of modulation index is always between zero and one.
Since in FM, amplitude of the earner is constant, the transmitted power is constant, independent of the modulation index. | 
The modulation index determines the number of significant pairs of sidebands in an FM signal. | In an AM signal, only two sidebands are produced, for any value of modulation index.
The amplitudes of the carrier and side bands vary with the modulation index and can be calculated with Bessel functions. | The amplitudes of the sidebands is dependent on the modulation index, and is always less than the amplitude of carrier.
The carrier or sideband amplitudes are zero at some modulation indices. | The sideband amplitude is never zero for any value of modulation index greater than zero.
The bandwidth of an FM signal is proportional to the modulation index. | The bandwidth of an AM signal is twice the highest modulating frequency.
For FM, the % of modulation is the ratio of the actual frequency deviation and the maximum.om permissible frequency deviation multiplied by 100. | For AM, % modulation is the ratio of amplitude of modulating voltage to the amplitude of the carrier multiplied by 100.
Notes: 𝑃_𝑇=𝑃_𝑐 [1+𝑚^2/2]

## Slide 96: Comparison of FM and AM
FM | AM
The main advantage of FM over AM is its noise immunity, as limiter stage in FM receiver clips off noise signals. | The AM system is more susceptible to noise and more affected by noise than FM.
The capture effect in FM allows the strongest signal on a frequency to dominate without interference from the other signal. | When two AM signals occupy the same frequency, both signals will generally be heard regardless of their relative signal strength.
In FM, greater transmitter efficiency can be realized using class-C amplifiers, as amplitude of FM signal is constant. | The efficiency of AM is less than that of FM due to use of class-B amplifier.
The bandwidth of FM signal is much under than the bandwidth of AM. The bandwidth of a typical FM channel is 200 kHz. | The bandwidth required to transmit AM signal is much less than that of FM typically 10 kHz in AM broadcasting.
Notes: 𝑃_𝑇=𝑃_𝑐 [1+𝑚^2/2]